## Slide 1: 24-783 Lecture 13

## Slide 2
Binary STL
Picking

## Slide 3: Dealing with a binary data file
Binary file
Just a sequence of numbers.
Not in the human-readable format.
Program needs to interpret.

## Slide 4: Binary dump
Often used for inspecting a binary file.
Prints 256 numbers per chunk, 16 numbers per line.
Numbers shown in hexa-decimal number.
00000000| 64 86 06 00 7e 57 9e 56 3f 05 00 00 24 00 00 00
00000010| 00 00 00 00 2e 64 72 65 63 74 76 65 00 00 00 00
00000020| 00 00 00 00 2f 00 00 00 04 01 00 00 00 00 00 00
00000030| 00 00 00 00 00 00 00 00 00 0a 10 00 2e 64 65 62
00000040| 75 67 24 53 00 00 00 00 00 00 00 00 bc 00 00 00
00000050| 33 01 00 00 00 00 00 00 00 00 00 00 00 00 00 00
00000060| 40 00 10 42 2e 72 64 61 74 61 00 00 00 00 00 00
00000070| 00 00 00 00 54 00 00 00 ef 01 00 00 00 00 00 00
00000080| 00 00 00 00 00 00 00 00 40 00 40 40 2e 74 65 78
00000090| 74 24 6d 6e 00 00 00 00 00 00 00 00 c8 01 00 00
000000a0| 43 02 00 00 0b 04 00 00 00 00 00 00 13 00 00 00
000000b0| 20 00 50 60 2e 78 64 61 74 61 00 00 00 00 00 00
000000c0| 00 00 00 00 18 00 00 00 c9 04 00 00 e1 04 00 00
000000d0| 00 00 00 00 01 00 00 00 40 00 30 40 2e 70 64 61
000000e0| 74 61 00 00 00 00 00 00 00 00 00 00 18 00 00 00
000000f0| eb 04 00 00 03 05 00 00 00 00 00 00 06 00 00 00

## Slide 5: Binary dump program.
#include <stdio.h>
void PrintDump(const char fn[])
{
FILE *fp=fopen(fn,"rb");
if(nullptr!=fp)
{
long long int offset=0,readSize;
unsigned char buf[256];
while(0<(readSize=fread(buf,1,256,fp)))
{
for(int i=0; i<256; i+=16)
{
printf("%08llx|",offset+i);
for(int j=0; j<16; ++j)
{
if(readSize<=i+j)
{
break;
}
printf(" %02x",buf[i+j]);
}
printf("\n");
}
printf("\n");
offset+=256;
}
fclose(fp);
}
else
{
printf("Cannot open file.\n");
}
}
int main(int argc,char *argv[])
{
if(2==argc)
{
PrintDump(argv[1]);
}
else
{
printf("Usage: dump.exe <filename>\n");
return 0;
}
}

## Slide 6: Hexa-decimal number
1 digit represents from 0-15. 0 => 0 8 => 8 1 => 1 9 => 9 2 => 2 A => 10 3 => 3 B => 11 4 => 4 C => 12 5 => 5 D => 13 6 => 6 E => 14 7 => 7 F => 15
In C++, you can write a hexadecimal number by adding 0x in front.
Example: Hexa-Decimal Decimal 0x0A => 0*161 + 10*160 = 10 0x80 => 8*161 + 0*160 = 128 0xA0 => 10*161 + 0*160 = 160 0xFF => 15*161 + 15*160 = 255 0x100 => 1*162 + 0*161 + 0*160 = 256

## Slide 7: Binary STL file
Change directory to ~/24783 and type: svn checkout https://ramennoodle.me.cmu.edu/svn/teaching/data
You can download some sample STLs (ASCII and Binary)
We will add more sample data files. When you start an assignment, you can change directory to ~/24783/data, and type: svn update

## Slide 8: Binary STL
STL: Probably THE WORST possible data format for representing a polygonal-mesh geometry.
No color, no topological information, only grouping up to 65536 groups (and most CAD packages do not bother writing a grouping information).
Binary STL format is limited to the single-precision.
Only advantage: Easy to display. Absolutely no other advantage.
As usual, the worst possible data format becomes a industry standard.

## Slide 9: Binary STL file
80 bytes Comment in ASCII characters
4 bytes Number of triangles
50 bytes Normal, Three (x,y,z) coords, and volume id.
50 bytes Normal, Three (x,y,z) coords, and volume id.
:
00000000| 62 69 6e 73 74 6c 53 54 4c 20 67 65 6e 65 72 61
00000010| 74 65 64 20 62 79 20 50 6f 6c 79 67 6f 6e 43 72
00000020| 65 73 74 20 65 64 69 74 6f 72 2e 20 20 20 20 20
00000030| 20 20 20 20 20 20 20 20 20 20 20 20 20 20 20 20
00000040| 20 20 20 20 20 20 20 20 20 20 20 20 20 20 20 20
00000050| 50 00 00 00 00 00 00 80 00 00 80 bf 00 00 00 80
00000060| 15 ef c3 be 00 00 80 bf 5e 83 6c bf f3 04 35 bf
00000070| 00 00 80 bf f3 04 35 bf 00 00 a0 c0 00 00 80 bf
00000080| 00 00 a0 c0 00 00 00 00 00 80 00 00 00 80 00 00
00000090| 80 bf 00 00 a0 40 00 00 80 bf 00 00 a0 c0 00 00
000000a0| a0 c0 00 00 80 3f 00 00 a0 c0 00 00 a0 40 00 00
000000b0| 80 3f 00 00 a0 c0 00 00 00 00 80 3f 00 00 00 00
000000c0| 00 00 00 00 00 00 a0 40 00 00 80 bf 00 00 a0 40
000000d0| 00 00 a0 40 00 00 80 3f 00 00 a0 c0 00 00 a0 40
000000e0| 00 00 80 3f 00 00 a0 40 00 00 00 00 00 00 00 00
000000f0| 00 00 00 00 80 3f 00 00 a0 c0 00 00 80 bf 00 00
First 80 bytes
# of triangles

## Slide 10: 50 bytes for a triangle
+0 4 bytes Normal X
+4 4 bytes Normal Y
+8 4 bytes Normal Z
+12 4 bytes x0
+16 4 bytes y0
+20 4 bytes z0
+24 4 bytes x1
+28 4 bytes y1
+32 4 bytes z1
+36 4 bytes x2
+40 4 bytes y2
+44 4 bytes z2
+48 2 bytes Volume ID

## Slide 11: Reading a binary data file
Open a file with “rb” mode.
Use fread function to read binary data. fread(buf,unit,count,fp); buf unsigned char pointer to the data buffer. unit Unit size. Usually 1. count Number of units to read. fp File pointer. It reads unit*count bytes from the file fp.

## Slide 12: Interpreting a binary data file.
Everything is in an array of unsigned char.
Converting four bytes of unsigned chars to an unsigned integer: (Input is const unsigned char dat[4], output is unsigned int value.) unsigned char b0=dat[0]; unsigned char b1=dat[1]; unsigned char b2=dat[2]; unsigned char b3=dat[3]; unsigned int value=b0+b1*0x100+b2*0x10000+b3*0x1000000;
Converting four bytes of unsigned chars (in IEEE standard floating-point format) to a float: (Input is const unsigned char dat[4], output is float value.) const float *fPtr=(const float *)dat; float value=*fPtr;

## Slide 13: What if the world is not an Intel world?
The byte-order problem. (Little endian vs. Big endian.)
Little endian: Least-Significant Byte appears first. Hexa-decimal number 0x0102A0B0 will be stored as: B0 A0 02 01
Big endian: Most-Significant Byte appears first. Hexa-decimal number 0x0102A0B0 will be stored as: 01 02 A0 B0
To write a general-purpose binary-reading code, you need to be aware of the endian-ness of the file and the CPU.

## Slide 14
Historically, Intel CPUs have been using little endian, and Motorola CPUs have been using big endian.
ARM uses bi-endian, which can switch the endian-ness. But, probably the program may not know until run time.
Hopefully the CPU uses same endian-ness for all data types.

## Slide 15: Question:
How can you identify the endian-ness of the CPU in C++? bool CPUisLittleEndian(void) { ? }

## Slide 16: Endian-ness of a Binary STL
Known to be Little-Endian. Compatible with Intel CPU.
This integer-conversion works regardless of the CPU. (Input is const unsigned char dat[4], output is unsigned int value.) unsigned char b0=dat[0]; unsigned char b1=dat[1]; unsigned char b2=dat[2]; unsigned char b3=dat[3]; unsigned int value=b0+b1*0x100+b2*0x10000+b3*0x1000000;
If CPU’s endian-ness is big-endian, floating-point conversion needs to be: if(true==CPUisLittleEndian()) { auto *fPtr=(const float *)dat; value=*fPtr; } else { auto *valuePtr=(unsigned char *)(&value); valuePtr[0]=dat[3]; valuePtr[1]=dat[2]; valuePtr[2]=dat[1]; valuePtr[3]=dat[0]; }
Copy byes to where the value is stored in the reverse order.

## Slide 17
binary_stl.h
#ifndef BINARY_STL_IS_INCLUDED
#define BINARY_STL_IS_INCLUDED
#include "vector"
bool LoadBinaryStl(std::vector <float> &vtx,std::vector <float> &nom,const char fn[]);
bool CPUisLittleEndian(void);
int BinaryToInt(const unsigned char dw[4]);
float BinaryToFloat(const unsigned char dw[4]);
#endif

## Slide 18
binary_stl.cpp
#include "binary_stl.h"
bool CPUisLittleEndian(void)
{
unsigned int one=1;
auto *dat=(const unsigned char *)&one;
if(1==dat[0])
{
return true;
}
return false;
}
int BinaryToInt(const unsigned char dw[4])
{
int b0=(int)dw[0];
int b1=(int)dw[1];
int b2=(int)dw[2];
int b3=(int)dw[3];
return b0+b1*0x100+b2*0x10000+b3*0x1000000;
}
float BinaryToFloat(const unsigned char dw[4])
{
if(true==CPUisLittleEndian())
{
const float *fPtr=(const float *)dw;
return *fPtr;
}
else
{
float value;
auto *valuePtr=(unsigned char *)&value;
valuePtr[0]=dw[3];
valuePtr[1]=dw[2];
valuePtr[2]=dw[1];
valuePtr[3]=dw[0];
return value;
}
}
If the endian-ness of the CPU matches the endian-ness of the STL, the bytes are already ordered. No conversion necessary.
If the endian-ness of the CPU is reverse of the endian-ness of the STL, the bytes are reversed. First reverse the bytes and then convert.
Incoming bytes are little-endian. This is universal conversion to an unsigned integer.

## Slide 19
binary_stl.cpp
void AddBinaryStlTriangle(std::vector <float> &vtx,std::vector <float> &nom,const unsigned char buf[50])
{
float nx=BinaryToFloat(buf),ny=BinaryToFloat(buf+4),nz=BinaryToFloat(buf+8);
nom.push_back(nx);
nom.push_back(ny);
nom.push_back(nz);
nom.push_back(nx);
nom.push_back(ny);
nom.push_back(nz);
nom.push_back(nx);
nom.push_back(ny);
nom.push_back(nz);
vtx.push_back(BinaryToFloat(buf+12));
vtx.push_back(BinaryToFloat(buf+16));
vtx.push_back(BinaryToFloat(buf+20));
vtx.push_back(BinaryToFloat(buf+24));
vtx.push_back(BinaryToFloat(buf+28));
vtx.push_back(BinaryToFloat(buf+32));
vtx.push_back(BinaryToFloat(buf+36));
vtx.push_back(BinaryToFloat(buf+40));
vtx.push_back(BinaryToFloat(buf+44));
// buf[48] and buf[49] are volume identifier, which is usually not used.
}

## Slide 20
binary_stl.cpp
void LoadBinaryStl(std::vector <float> &vtx,std::vector <float> &nom,const char fn[])
{
FILE *fp=fopen(fn,"rb");
if(nullptr!=fp)
{
unsigned char title[80];
fread(title,1,80,fp); // Skip title
unsigned char dw[4];
fread(dw,4,1,fp); // Read 4 bytes
auto nTri=BinaryToInt(dw);
printf("%d triangles\n",nTri);
int nTriActual=0;
vtx.clear();
nom.clear();
for(int i=0; i<nTri; ++i)
{
unsigned char buf[50]; // 50 bytes per triangle
if(50==fread(buf,1,50,fp))
{
AddBinaryStlTriangle(vtx,nom,buf);
++nTriActual;
}
else
{
break;
}
}
printf("Actually read %d\n",nTriActual);
fclose(fp);
}
}

## Slide 21
Alternative way of reading normal vectors and vertex positions (if you know that the CPU’s endianness is same as the STL’s)
int nTriActual=0;
vtx.clear();
nom.clear();
for(int i=0; i<nTri; ++i)
{
float buf[12];
if(48==fread(buf,1,48,fp))
{
nom.push_back(buf[0]); nom.push_back(buf[1]); nom.push_back(buf[2]);
nom.push_back(buf[0]); nom.push_back(buf[1]); nom.push_back(buf[2]);
nom.push_back(buf[0]); nom.push_back(buf[1]); nom.push_back(buf[2]);
vtx.push_back(buf[ 3]); vtx.push_back(buf[ 4]); vtx.push_back(buf[ 5]);
vtx.push_back(buf[ 6]); vtx.push_back(buf[ 7]); vtx.push_back(buf[ 8]);
vtx.push_back(buf[ 9]); vtx.push_back(buf[10]); vtx.push_back(buf[11]);
unsigned char skip[2];
fread(skip,1,2,fp);
++nTriActual;
}
}

## Slide 22: How far the view point should be away from where?
For rendering, the following information is needed.
  Size of the STL model. Typically use the diagonal length of the bounding box.
  Center of the STL model. Can be center of gravity, or we can go with the center of the bounding box.
  Need to write a function for getting the bounding box (min and max of XYZ)
  Then,

## Slide 23
The camera should look at the center of the bounding box of the STL model.
Also sufficiently far away from the model compared to the diameter of the bounding box.
FOV
d/2
Example: (d/2)/sin(FOV/2) If the diameter is 45 deg, 0.5/sin(22.5deg)=1.31 times diameter.

## Slide 24: Add GetBoundingBox function in binary_stl.h and binary_stl.cpp
#include <ysclass.h>
void GetBoundingBox(YsVec3 &min,YsVec3 &max,std::vector <float> &vtx);
void GetBoundingBox(YsVec3 &min,YsVec3 &max,std::vector <float> &vtx)
{
YsRect3 rect;
if(0<vtx.size()/3)
{
min.Set(vtx[0],vtx[1],vtx[2]);
max.Set(vtx[0],vtx[1],vtx[2]);
for(int i=0; i<vtx.size()/3; ++i)
{
// min[0]=(min[0]<vtx[i*3] ? min[0] : vtx[i*3]);
YsMakeSmaller<double>(min[0],vtx[i*3]);
YsMakeSmaller<double>(min[1],vtx[i*3+1]);
YsMakeSmaller<double>(min[2],vtx[i*3+2]);
YsMakeGreater<double>(max[0],vtx[i*3]);
YsMakeGreater<double>(max[1],vtx[i*3+1]);
YsMakeGreater<double>(max[2],vtx[i*3+2]);
}
}
else
{
min=YsVec3::Origin();
max=YsVec3::Origin();
}
}

## Slide 25
Member variables of FsLazyWindowApplication
Initialize function: Read .STL file, cache bounding box, calculate t and d.
std::vector <float> vtx,nom,col;
YsVec3 bbx[2];
/* virtual */ void FsLazyWindowApplication::Initialize(int argc,char *argv[])
{
if(2<=argc)
{
::LoadBinaryStl(vtx,nom,argv[1]);
for(int i=0; i<vtx.size()/3; ++i)
{
col.push_back(0.5f);
col.push_back(0.5f);
col.push_back(0.5f);
col.push_back(1.0f);
}
GetBoundingBox(bbx[0],bbx[1],vtx);
t=(bbx[0]+bbx[1])/2.0;
d=(bbx[1]-bbx[0]).GetLength()*1.2;
printf("Target %s\n",t.Txt());
printf("Diagonal %lf\n",d);
}
}

## Slide 26: Changes in the Draw function
glClear(GL_COLOR_BUFFER_BIT|GL_DEPTH_BUFFER_BIT);
glEnable(GL_DEPTH_TEST);
int wid,hei;
FsGetWindowSize(wid,hei);
auto aspect=(double)wid/(double)hei;
glViewport(0,0,wid,hei);
glMatrixMode(GL_PROJECTION);
glLoadIdentity();
gluPerspective(45.0,aspect,d/10.0,d*2.0);
YsMatrix4x4 globalToCamera=Rc;
globalToCamera.Invert();
YsMatrix4x4 modelView; // need #include ysclass.h
modelView.Translate(0,0,-d);
modelView*=globalToCamera;
modelView.Translate(-t);
GLfloat modelViewGl[16];
modelView.GetOpenGlCompatibleMatrix(modelViewGl);
glMatrixMode(GL_MODELVIEW);
glLoadIdentity();
GLfloat lightDir[]={0,1/sqrt(2.0f),1/sqrt(2.0f),0};
glLightfv(GL_LIGHT0,GL_POSITION,lightDir);
glEnable(GL_COLOR_MATERIAL);
glEnable(GL_LIGHTING);
glEnable(GL_LIGHT0);
glMultMatrixf(modelViewGl);
glEnableClientState(GL_VERTEX_ARRAY);
glEnableClientState(GL_NORMAL_ARRAY);
glEnableClientState(GL_COLOR_ARRAY);
glColorPointer(4,GL_FLOAT,0,col.data());
glNormalPointer(GL_FLOAT,0,nom.data());
glVertexPointer(3,GL_FLOAT,0,vtx.data());
glDrawArrays(GL_TRIANGLES,0,vtx.size()/3);
glDisableClientState(GL_VERTEX_ARRAY);
glDisableClientState(GL_NORMAL_ARRAY);
glDisableClientState(GL_COLOR_ARRAY);
FsSwapBuffers();

## Slide 27: Identifying ASCII or Binary
When you have a binary STL file, it is nearly impossible to check if it is really a binary STL file, or something else, or a corrupted binary STL file.
But, if you know that the file is an STL file, you can reliably identify if it is an ASCII STL or Binary STL.
An ASCII STL file includes some keywords, “solid”, “facet”, “loop”, and “vertex”.
Read first 1000 bytes of the file, and check if these keywords are included.
It is no more than a guess, but all you can do is to guess.

## Slide 28
bool IsAsciiStl(const char fn[])
{
FILE *fp=fopen(fn,"rb");
if(nullptr!=fp)
{
char buf[1024];
fread(buf,1,1024,fp);
fclose(fp);
bool solid,facet,loop,vertex;
solid=false;
facet=false;
loop=false;
vertex=false;
for(i=0; i<1018; i++)
{
if(strncmp(buf+i,"solid",5)==0)
{
solid=true;
}
else if(strncmp(buf+i,"facet",5)==0)
{
facet=true;
}
else if(strncmp(buf+i,"loop",4)==0)
{
loop=true;
}
else if(strncmp(buf+i,"vertex",6)==0)
{
vertex=true;
}
}
if(true==solid && true==facet && true==loop && true==vertex)
{
return true;
}
}
return false;
}
In binary_stl.cpp. Function prototype in binary_stl.h

## Slide 29
After adding IsAsciiSTL function:
/* virtual */ void FsLazyWindowApplication::BeforeEverything(int argc,char *argv[])
{
if(2<=argc)
{
if(true==::IsAsciiStl(argv[1]))
{
printf("It is not a binary stl!\n");
return;
}
LoadBinaryStl(argv[1]);
}
}

## Slide 31: Polygonal Mesh
Minimum information is a set of disconnected polygons (eg. STL data)
Minimum information is good for visualizing.
Useless for other purposes.

## Slide 32: Better-Than Minimum Information
Vertices & Connections
A list of vertices
A list of polygons, each of which has a chain of vertices
v0
v1
v2
v3
v4
v5
v6
v7
v8
v9
f0
f1
f2
f3
f4
f5
f6
f0 {v1, v0, v3, v4}
f1 {v2, v1, v4}
f2 {v4, v3, v6}
f3 {v2, v4, v5}
f4 {v5, v4, v6, v7}
f5 {v7, v8, v5}
f6 {v9, v7, v6}

## Slide 33: More useful information
Polygons are search-able from a vertex or an edge.
Can be done by keeping a hash table.
v0
v1
v2
v3
v4
v5
v6
v7
v8
v9
v0 {f0}
v1 {f0, f1}
v2 {f1, f3}
v3 {f0, f2}
v4 {f0, f1, f2, f3, f4}
v5 {f3, f4, f5}
:
e(v0,v1) {f0}
e(v1,v2) {f1}
e(v1,v4) {f0, f1} e(v3,v4) {f0, f2}
e(v5,v7) {f4, f5}
:
f0
f1
f2
f3
f4
f5
f6

## Slide 34: Richer information
Constraint edges
  Also called feature edges
  Chain of vertices
  Automatic detection is still a hot research topic
Face groups
  Also called segments
  Group of polygons
  In many cases dual of constraint edges (constraint edges are the boundaries between face groups)
  Automatic segmentation that works for general geometry does not exist yet.

## Slide 35: Closed (manifold), open, and non-manifold polygonal meshes
A polygonal mesh can be classified as:
Closed mesh (Manifold mesh)
  Every edge is used by two polygons. (Two-manifold-ness)
  Necessary condition to represent a solid.
Open mesh
  Some edges are used by only one polygon, all other edges are used by two polygons.
  Good for fabric, sheet-metal, terrain-elevation models.
Non-manifold mesh
  Some edges may be used by more than two polygons.
  Used for an assembly of sheet-metal parts, assembly of multiple volumes.

## Slide 36: Implementation
When a modification is made to the data structure, topology (connection) tables must also be updated.
If the outside code can directly modify the raw data structure, the table may become out of sync.
Raw data structure must be hidden from the outside, or only allow access as constant.

## Slide 37: Implementing a Polygonal-Mesh data structure
Decision: What background data structure to use?
  Doubly-Linked list? (std::list)
  Variable-Length array? (std::vector)
Let's try a linked list.

## Slide 38: Does it work?
class PolygonalMesh
{
protected:
class Vertex
{
public:
YsVec3 pos;
};
private:
std::list <Vertex> vtxList;
public:
class VertexHandle
{
friend class PolygonalMesh;
private:
std::list<Vertex>::iterator vtxPtr;
public:
VertexHandle(){}; // C++11 VertexHandle()=default;
VertexHandle(std::nullptr_t);
void operator=(std::nullptr_t);
bool operator==(std::nullptr_t) const;
bool operator!=(std::nullptr_t) const;
};
VertexHandle AddVertex(const YsVec3 &pos);
YsVec3 GetVertexPosition(VertexHandle vtHd) const;
};
inline bool operator==(std::nullptr_t,PolygonalMesh::VertexHandle);
inline bool operator!=(std::nullptr_t,PolygonalMesh::VertexHandle);
What's this?

## Slide 39: Iterator
Before range-based for, this was what people were doing:
  for(auto iter=container.begin(); container.end()!=iter; ++iter)
  {
  auto value=*iter;
  // Do something fun with the value.
  }
Before auto, it was messier:
  for(std::vector <int> iter=container.begin();
  container.end()!=iter;
  ++iter)
  {
  int value=*iter;
  // Do something fun with the value.
  }
Not it can be written as:
  for(auto value : container)
  {
  }

## Slide 40: Iterator
If you define your own iterator class that satisfies certain requirements, you can use range-based for with your own class.

## Slide 41: Question
Can the iterator help in this situation?

## Slide 42: Does it work?
class PolygonalMesh
{
protected:
class Vertex
{
public:
YsVec3 pos;
};
private:
std::list <Vertex> vtxList;
public:
class VertexHandle
{
friend class PolygonalMesh;
private:
std::list<Vertex>::iterator vtxPtr;
public:
VertexHandle(){}; // C++11 VertexHandle()=default;
VertexHandle(std::nullptr_t);
void operator=(std::nullptr_t)
{
return vtxPtr==What?
}
bool operator==(std::nullptr_t) const;
bool operator!=(std::nullptr_t) const;
};
VertexHandle AddVertex(const YsVec3 &pos);
YsVec3 GetVertexPosition(VertexHandle vtHd) const;
};
VertexHandle needs to know who owns this handle. It is fine as long as you are dealing with thousands of vertices. If you get millions of vertices, it's not. Major weakness of the standard iterator.

## Slide 43: Does it work?
class PolygonalMesh
{
protected:
class Vertex
{
public:
YsVec3 pos;
};
private:
std::list <Vertex> vtxList;
public:
class VertexHandle
{
friend class PolygonalMesh;
private: std::list <Vertex> *vtxListptr;
std::list<Vertex>::iterator vtxPtr;
public:
VertexHandle(){}; // C++11 VertexHandle()=default;
VertexHandle(std::nullptr_t);
void operator=(std::nullptr_t)
{
return vtxPtr==vtxListPtr->end();
}
bool operator==(std::nullptr_t) const;
bool operator!=(std::nullptr_t) const;
};
VertexHandle AddVertex(const YsVec3 &pos);
YsVec3 GetVertexPosition(VertexHandle vtHd) const;
};
VertexHandle always needs to know the owner.
I want polygons to store std::vector of VertexHandles.
I can do it this way, but a VertexHandle cannot independently created. UGLY!

## Slide 44: How about std::vector?
#ifndef POLYGONALMESH_IS_INCLUDED
#define POLYGONALMESH_IS_INCLUDED
#include <vector>
#include <ysclass.h>
class PolygonalMesh
{
protected:
class Vertex
{
public:
YsVec3 pos;
};
private:
std::vector <Vertex> vtxList;
public:
class VertexHandle
{
friend class PolygonalMesh;
private:
int vtxIdx;
VertexHandle(){}; // C++11 VertexHandle()=default;
VertexHandle(std::nullptr_t);
void operator=(std::nullptr_t);
bool operator==(std::nullptr_t) const;
bool operator!=(std::nullptr_t) const;
};
VertexHandle AddVertex(const YsVec3 &pos);
YsVec3 GetVertexPosition(VertexHandle vtHd) const;
};
inline bool operator==(std::nullptr_t,PolygonalMesh::VertexHandle);
inline bool operator!=(std::nullptr_t,PolygonalMesh::VertexHandle);
#endif

## Slide 45: Go with std::vector for now?
It does work. Somewhat.
  We can define our handle so that index of -1 means a null handle.
  We can independently create a vertex handle.
  Can nullify without the owner.
  The size of a handle can be 4 bytes.
Two problems:
  Pointers to the vertices move when the array grows.
  We cannot really delete vertices because they may be used from polygons. We can only add a flag like: bool deleted;

## Slide 46: How about this?
#ifndef POLYGONALMESH_IS_INCLUDED
#define POLYGONALMESH_IS_INCLUDED
#include <list>
#include <ysclass.h>
class PolygonalMesh
{
protected:
class Vertex
{
public:
YsVec3 pos;
};
private:
mutable std::list <Vertex> vtxList;
public:
class VertexHandle
{
friend class PolygonalMesh;
private:
std::list <Vertex>::iterator vtxPtr;
VertexHandle(){}; // C++11 VertexHandle()=default;
bool operator==(const VertexHandle &vtHd) const;
bool operator!=(const VertexHandle &vtHd) const;
};
VertexHandle AddVertex(const YsVec3 &pos);
VertexHandle NullVertex(void) const;
YsVec3 GetVertexPosition(VertexHandle vtHd) const;
};
#endif
Put the responsibility to define a null-vertex handle to the PolygonalMesh class.
Only one disadvantage is that the size of the vertex handle is governed by the size of the std::list<>::iterator.
I'm no fully happy, but it is the least ugly among these three.

## Slide 47
We can think about the data structure better suited for this situation later.
For the time being, let's use std::list (doubly-linked list), but hide the background data structure so that it can be replaced later.

## Slide 48: Let's go with std::list
#ifndef POLYGONALMESH_IS_INCLUDED
#define POLYGONALMESH_IS_INCLUDED
#include <list>
#include <ysclass.h>
class PolygonalMesh
{
protected:
class Vertex
{
public:
YsVec3 pos;
};
private:
mutable std::list <Vertex> vtxList;
public:
class VertexHandle
{
friend class PolygonalMesh;
private:
std::list <Vertex>::iterator vtxPtr;
public:
inline bool operator==(const VertexHandle &vtHd) const;
inline bool operator!=(const VertexHandle &vtHd) const;
};
VertexHandle AddVertex(const YsVec3 &pos);
inline VertexHandle NullVertex(void) const;
YsVec3 GetVertexPosition(VertexHandle vtHd) const;
};
#endif

## Slide 49: Test what we have so far
#include "polygonalmesh.h"
int main(void)
{
PolygonalMesh s;
std::vector <PolygonalMesh::VertexHandle> vtHdArray;
vtHdArray.push_back(s.AddVertex(YsVec3::Origin()));
return 0;
}

## Slide 50: Adding polygons
Data structure: Same logic as vertices.
A polygon consists of an ordered set of vertices.
protected:
class Polygon
{
public:
std::vector <VertexHandle> vtHd;
};
private:
mutable std::list <Polygon> plgList;
public:
class PolygonHandle
{
friend class PolygonalMesh;
private:
std::list <Polygon>::iterator plgPtr;
public:
PolygonHandle(){}; // C++11 PolygonHandle()=default;
inline bool operator==(const PolygonHandle &plHd) const;
inline bool operator!=(const PolygonHandle &plHd) const;
};
PolygonHandle AddPolygon(int nPlVt,const VertexHandle plVtHd[]);
PolygonHandle AddPolygon(const std::vector <VertexHandle> &plVtHd);
inline PolygonHandle NullPolygon(void) const;
const std::vector <VertexHandle> GetPolygonVertex(PolygonHandle plHd) const;

## Slide 51: Test what we have so far
#include "polygonalmesh.h"
int main(void)
{
PolygonalMesh s;
std::vector <PolygonalMesh::VertexHandle> vtHdArray;
vtHdArray.push_back(s.AddVertex(YsVec3(-3,-3,-3)));
vtHdArray.push_back(s.AddVertex(YsVec3( 3,-3,-3)));
vtHdArray.push_back(s.AddVertex(YsVec3( 3,-3, 3)));
vtHdArray.push_back(s.AddVertex(YsVec3(-3,-3, 3)));
vtHdArray.push_back(s.AddVertex(YsVec3(-3, 3,-3)));
vtHdArray.push_back(s.AddVertex(YsVec3( 3, 3,-3)));
vtHdArray.push_back(s.AddVertex(YsVec3( 3, 3, 3)));
vtHdArray.push_back(s.AddVertex(YsVec3(-3, 3, 3)));
int plgVtx[6][4]=
{
{0,1,2,3},{7,6,5,4},{1,0,5,4},{2,1,5,6},{3,2,6,7},{0,3,7,4}
};
for(auto pv : plgVtx)
{
std::vector<PolygonalMesh::VertexHandle> plVtHd;
plVtHd.push_back(vtHdArray[pv[0]]);
plVtHd.push_back(vtHdArray[pv[1]]);
plVtHd.push_back(vtHdArray[pv[2]]);
plVtHd.push_back(vtHdArray[pv[3]]);
s.AddPolygon(plVtHd);
}
return 0;
}

## Slide 52: Adding Access Functions
Let’s implement the following functions, and
Add the following in the test.
long long int GetNumVertex(void) const;
bool MoveToNextVertex(VertexHandle &vtHd) const;
long long int GetNumPolygon(void) const;
bool MoveToNextPolygon(PolygonHandle &plHd) const;
printf("%d vertices\n",(int)s.GetNumVertex());
printf("%d polygons\n",(int)s.GetNumPolygon());
for(auto vtHd=s.NullVertex(); true==s.MoveToNextVertex(vtHd); )
{
auto pos=s.GetVertexPosition(vtHd);
printf("Vertex %lf %lf %lf\n",pos.x(),pos.y(),pos.z());
}
for(auto plHd=s.NullPolygon(); true==s.MoveToNextPolygon(plHd); )
{
auto plVtHd=s.GetPolygonVertex(plHd);
printf("Polygon with %d vertices.\n",(int)plVtHd.size());
}

## Slide 53: Want to add a topological information
In the current format, you can find a set of vertices from a polygon.
But, what if you want to find a set of polygons from a vertex?
Visit all polygons to check if the polygon is using the vertex? Will take O(N). If you need to do it for each vertex, the order will be O(N2).
Can we find a set of polygons from a vertex at O(1) time?
But, we don’t want to spend memory space when this information is unnecessary.

## Slide 54: Use Hash Table
Let’s assign a unique search key for each vertex.
The search key will never be recycled. It constantly increments.
It is persistent within one execution of the program.
Make a hash table (std::unordered_map) from the vertex search key to std::vector <PolygonHandle>.
The table is updated when a polygon is added (later also when a polygon is modified or deleted.)

## Slide 55: Additions in the polygonalmesh.h
class PolygonalMesh
{
protected:
unsigned int searchKeySeed;
public:
PolygonalMesh();
protected:
class Vertex
{
public:
YsVec3 pos;
unsigned int searchKey;
};
public:
unsigned int GetSearchKey(VertexHandle vtHd) const;
std::vector <PolygonHandle> FindPolygonFromVertex(VertexHandle vtHd) const;
protected:
std::unordered_map <unsigned int,VertexHandle> vtxSearch;
protected:
std::unordered_map <unsigned int,std::vector <PolygonHandle> > vtKeyToPlg;

## Slide 56: Changes in polygonalmesh.cpp
PolygonalMesh::PolygonalMesh()
{
searchKeySeed=1;
}
PolygonalMesh::VertexHandle PolygonalMesh::AddVertex(const YsVec3 &pos)
{
Vertex vtx;
vtx.pos=pos;
vtx.searchKey=searchKeySeed;
vtxList.push_back((Vertex &&)vtx);
VertexHandle vtHd;
vtHd.vtxPtr=vtxList.end();
vtHd.vtxPtr--;
vtxSearch[searchKeySeed]=vtHd;
++searchKeySeed;
return vtHd;
}
PolygonalMesh::PolygonHandle PolygonalMesh::AddPolygon(int nPlVt,const VertexHandle plVtHd[])
{
Polygon plg;
plg.vtHd.resize(nPlVt);
for(int i=0; i<nPlVt; ++i)
{
plg.vtHd[i]=plVtHd[i];
}
plgList.push_back((Polygon &&)plg);
PolygonHandle plHd;
plHd.plgPtr=plgList.end();
--plHd.plgPtr;
for(int i=0; i<nPlVt; ++i)
{
vtKeyToPlg[GetSearchKey(plVtHd[i])].push_back(plHd);
}
return plHd;
}

## Slide 57: Changes in polygonalmesh.cpp
unsigned int PolygonalMesh::GetSearchKey(VertexHandle vtHd) const
{
if(NullVertex()==vtHd)
{
return 0xffffffff;
}
return vtHd.vtxPtr->searchKey;
}
std::vector <PolygonalMesh::PolygonHandle> PolygonalMesh::FindPolygonFromVertex(VertexHandle vtHd) const
{
auto found=vtKeyToPlg.find(GetSearchKey(vtHd));
if(vtKeyToPlg.end()!=found)
{
return found->second;
}
std::vector <PolygonHandle> vtPlHd;
return vtPlHd;
}

## Slide 58: Modify test
printf("%d vertices\n",(int)s.GetNumVertex());
printf("%d polygons\n",(int)s.GetNumPolygon());
for(auto vtHd=s.NullVertex(); true==s.MoveToNextVertex(vtHd); )
{
auto pos=s.GetVertexPosition(vtHd);
auto vtPlHd=s.FindPolygonFromVertex(vtHd);
printf("Vertex %lf %lf %lf used by %d polygons.\n",pos.x(),pos.y(),pos.z(),(int)vtPlHd.size());
}
for(auto plHd=s.NullPolygon(); true==s.MoveToNextPolygon(plHd); )
{
auto plVtHd=s.GetPolygonVertex(plHd);
printf("Polygon with %d vertices.\n",(int)plVtHd.size());
}

## Slide 59: Add normal vector and color per polygon.
Next goal: Adding LoadStl function.
Let’s add color and normal per polygon, and access functions.
YsColor class: Please see comment lines in public/src/ysclass/src/ysproperty.h for details.
protected:
class Polygon
{
public:
std::vector <VertexHandle> vtHd;
YsVec3 nom;
YsColor col;
};
public:
bool SetPolygonColor(PolygonHandle plHd,YsColor col);
YsColor GetColor(PolygonHandle plHd) const;
bool SetPolygonNormal(PolygonHandle plHd,const YsVec3 &nom);
YsVec3 GetNormal(PolygonHandle plHd) const;

## Slide 60: Then add LoadBinaryStl function
Copy some functions from binary_stl.cpp, and make LoadBinStl function of PolygonalMesh class.
public:
bool LoadBinStl(const char fn[]);
private:
bool CPUisLittleEndian(void);
int BinaryToInt(const unsigned char dw[4]);
float BinaryToFloat(const unsigned char dw[4]);
void AddBinaryStlTriangle(const unsigned char buf[50]);
public:
void GetBoundingBox(YsVec3 &min,YsVec3 &max) const;
void GetBoundingBox(YsVec3 bbx[2]) const;

## Slide 61: Replace the data structure of the STL viewer
Instead of directly reading STL into vertex arrays, load into PolygonalMesh data structure, and then make vertex arrays.
void FsLazyWindowApplication::Initialize(int argc,char *argv[])
{
if(2<=argc && true==mesh.LoadBinStl(argv[1]))
{
RemakeVertexArray();
mesh.GetBoundingBox(bbx[0],bbx[1]);
t=(bbx[0]+bbx[1])/2.0;
d=(bbx[1]-bbx[0]).GetLength()*1.2;
printf("Target %s\n",t.Txt());
printf("Diagonal %lf\n",d);
}
}

## Slide 62: Replace the data structure of the STL viewer
RemakeVertexArray function
void FsLazyWindowApplication::RemakeVertexArray(void)
{
for(auto plHd=mesh.NullPolygon(); true==mesh.MoveToNextPolygon(plHd); )
{
auto plVtHd=mesh.GetPolygonVertex(plHd);
auto plCol=mesh.GetColor(plHd);
auto plNom=mesh.GetNormal(plHd);
// Let's assume every polygon is a triangle for now.
if(3==plVtHd.size())
{
for(int i=0; i<3; ++i)
{
auto vtPos=mesh.GetVertexPosition(plVtHd[i]);
vtx.push_back(vtPos.xf());
vtx.push_back(vtPos.yf());
vtx.push_back(vtPos.zf());
nom.push_back(plNom.xf());
nom.push_back(plNom.yf());
nom.push_back(plNom.zf());
col.push_back(plCol.Rf());
col.push_back(plCol.Gf());
col.push_back(plCol.Bf());
col.push_back(plCol.Af());
}
}
}
}

## Slide 63: Picking
Identifying which primitive is under the mouse cursor.
Possible options:
  Using OpenGL’s picking feature – Very poorly designed. May not be supported in the newer versions.
  Drawing primitives in different color, and then check the color of the pixel under the mouse cursor – The actual RGB value written to the pixel may be reduced to as low as 12 bits. The identification information may be lost.
  Transform mouse pointer to a 3D line by the inverse of projection and view matrix, and calculate intersection with the primitives. - The most reliable. Can easily be parallelized.

## Slide 64: Projection transformation
OpenGL projection transforms a view frustum into a cube (-1,-1,-1)-(1,1,1)
Z direction will be inverted after the projection. Larger z means forward after the projection. (As shown in the thick arrow in the figure.)
z=-nearz
z=-farz
Projection Matrix
Z
Z

## Slide 65: Viewport transformation
(x,y)=(-1,-1) to (1,1) in the projected coordinate are linearly mapped to the viewport, which is in general same size as the window, specified by glViewport.
Z
Viewport
X
Y

## Slide 66: Mouse coordinate can be inverse-transformed to a line.
Z
Viewport
X
Y
z=-nearz
z=-farz
Projection Matrix
Z
Z

## Slide 67: Transforming a mouse coordinate to a 3D line
Normalize window coordinate (xs,ys) to (-1,-1)-(1,1) with respect to the viewport => (xv,yv)
Inverse-transform (xv,yv,-1) and (xv,yv,1) by the projection matrix => (xn,yn,zn), (xf,yf,zf)
Inverse-transform (xn,yn,zn) and (xf,yf,zf) by the model-view matrix => (x1,y1,z1), (x2,y2,z2)
Let’s draw it on the screen.

## Slide 68: Calculation
We need to go back and forth between the window and the 3D coordinate systems.
Need to take control of the projection matrix and viewport transformation.

## Slide 69: glutil.h
#ifndef GLUTIL_IS_INCLUDED
#define GLUTIL_IS_INCLUDED
#include <ysclass.h>
YsVec3 WindowToViewPort(int winWid,int winHei,int x,int y);
YsMatrix4x4 MakePerspective(const double fovy,const double aspect,const double nearz,const double farz);
YsMatrix4x4 MakeOrthogonal(
const double left,const double right,const double bottom,const double top,const double nearz,const double farz);
#endif

## Slide 70: glutil.cpp
#include "glutil.h"
YsVec3 WindowToViewPort(int winWid,int winHei,int x,int y) // Easy enough. Fill in class.
YsMatrix4x4 MakePerspective(const double fovy,const double aspect,const double nearz,const double farz)
{
float mat[16];
// Based on the formula listed in www.opengl.org
const float f=(float)(1.0/tan(fovy/2.0));
mat[0]=(float)(f/aspect); mat[4]=0; mat[ 8]=0; mat[12]=0;
mat[1]=0; mat[5]=(float)f; mat[ 9]=0; mat[13]=0;
mat[2]=0; mat[6]=0; mat[10]=(float)((farz+nearz)/(nearz-farz)); mat[14]=(float)((2.0*farz*nearz)/(nearz-farz));
mat[3]=0; mat[7]=0; mat[11]=-1; mat[15]=0;
YsMatrix4x4 tfm;
tfm.CreateFromOpenGlCompatibleMatrix(mat);
return tfm;
}
YsMatrix4x4 MakeOrthogonal(
const double left,const double right,const double bottom,const double top,const double nearz,const double farz)
{
float mat[16];
// Based on the formula listed in www.opengl.org
const double tx=-(right+left)/(right-left);
const double ty=-(top+bottom)/(top-bottom);
const double tz=-(farz+nearz)/(farz-nearz);
mat[0]=(float)(2.0/(right-left)); mat[4]=0; mat[ 8]=0; mat[12]=(float)tx;
mat[1]=0; mat[5]=(float)(2.0/(top-bottom)); mat[ 9]=0; mat[13]=(float)ty;
mat[2]=0; mat[6]=0; mat[10]=(float)(-2.0/(farz-nearz)); mat[14]=(float)tz;
mat[3]=0; mat[7]=0; mat[11]=0; mat[15]=1;
YsMatrix4x4 tfm;
tfm.CreateFromOpenGlCompatibleMatrix(mat);
return tfm;
}

## Slide 71: Picking
Change color of the picked polygon.
What needs to be done when the user clicks on the left button:
  Calculate a line from the mouse coordinate.
  Find the polygon that:
    intersects with the line, and
    in front of the camera, and
    nearest to the view point.
  Change the color of the polygon.

## Slide 72: Intersection of a line and a polygon
Plane-line intersection.
The intersecting point is on the boundary or inside of the polygon. (YsCheckInsidePolygon3)
/*! Templated version of YsCheckInsidePolygon3.
std::vector <YsVec3> or YsArray <YsVec3,N> can be given as plg.
It returns one of:
YSINSIDE Inside
YSOUTSIDE Outside
YSBOUNDARY On the boundary
YSUNKNOWNSIDE Cannot tell due to an error. */
inline YSSIDE YsCheckInsidePolygon3(const YsVec3 &ref,const YsConstArrayMask <YsVec3> &plg)
class YsPlane
{
public:
/*! Constructor that creates a plane from a point on the plane and a normal vector.
The incoming normal vector is normalized within this function. Therefore, the
vector does not have to be a unit vector.
\param o [In] A point on the plane
\param n [In] A normal vector */
YsPlane(const YsVec3 &o,const YsVec3 &n);
/*! If a given finite-length line intersects with the plane, it returns YSOK and the intersecting point is returns to crs. It returns YSERR otherwise.
\param crs [Out] Intersecting point
\param p1 [In] An end point of the finite-length line
\param p2 [In] The other end point of the finite-length line */
YSRESULT GetPenetration(YsVec3 &crs,const YsVec3 &p1,const YsVec3 &p2) const;

## Slide 73: Picking a point
What about picking a point? – Cannot calculate an intersection between a line and a point.
3D distance between a line and a point may not translate directly to the pixel distance.
Transform a 3D coordinate into a screen coordinate and compare.